| Safe Work Procedure |  |
| --- | --- |
| Department Bottleshop/Bars |  |
| Document number | Initial Issue date | Current version | Current Version Issue date | Next review date |
| Safe Work Procedure Title and basic description |  |
| Title: Moving Kegs Description: Safely Moving Kegs |
| Associated risk assessment title and location: |
| Describe the activity or process |  |
| Manual handling (manual tasks) is a job where you exert force to physically move an object or load. This exertion can be seen as you lifting, lowering, pulling, carrying, holding or restraining any object, or indeed a person. Examples include setting up furniture for a function, changing kegs, restocking shelves, restocking bars and carrying trays of glasses. Off pallet – placing on trolley or rolling individual kegs Off trolley – delivering to location |
| List all resources required including plant, chemicals, personal protective clothing and equipment, etc |  |
| Forklift Pallet Jack Trolley Personal Protective Equipment (as required) |
| List potential hazards and risk controls including specific precautions required |  |
| Potential Hazards: CO2 poisoning (cold room) Injury to back or other body parts (strains, sprains etc) Lacerations to extremities (aluminium burrs occur on the edges or seams of the kegs) Risk Controls: ‘Cellarguard’ CO2 detector and alarm system installed and operating Use gloves when handling kegs Forklift/pallet jack set at safe height Roll kegs on bottom edge when moving from pallet Only carry one keg on handheld trolley If lifting is essential, only a team lift would suffice Ensure correct clothing is worn when working in cold room for extended periods |

| List emergency shutdown instructions |  |
| --- | --- |
| Emergency stop button on Keg Lift |

| List clean up and waste disposal requirements |  |
| --- | --- |
| N/A |

| List legislation, standards and codes of practice used in the development of the SWP |  |
| --- | --- |
| Work Health & Safety Act 2011 |

| Supervisory approval, training, and review |  |
| --- | --- |
| Supervisor: | Signature: |
| List competency required – qualifications, certificates, licensing, training – e.g. course or instruction: Induction/OJT |
| SWP review date: | Responsibility for SWP review: |